MSDS No. egl puracite 04/01/2016

MATERIAL SAFETY DATA SHEET (MSDS)

egl puracite ltd.

Betws Washery Site, Pontamman,

Ammanford , Carmarthenshire SA18 2HQ

Tel: +44 1269 591477  Fax: +44 1269 597666

www.puracite.com

An ISO 9001: 2008 Certified Company

ANSI/AWWA B100 NSF Type 61 Approval

DRIED GRADED ANTHRACITE (FILTER MEDIA)

1.	Identification of Product

Name	...	...	...	Anthracite Filter Media (Puracite)

Synonyms	...	...	Low Gravity Filter Coal, Anthracite.

Intended uses	...	...	Filter Media, Potable and Waste Water Treatment, 							Carbon Additive, Re-carburiser, Brick Colourant.

CAS No.	…	…	8029-10-5 Anthracite.

H.S. Code.	…	…	2701 11 1000.

2.	Composition

Dried Graded Anthracite Comprising :- Fixed Carbon, Moisture , Ash, Volatile, Trace Sulphur.

Typical Chemical Analysis

| Fixed Carbon | c.92.5% DAF* |
| --- | --- |
| Volatile Matter | <7.5% |
| Ash Content | <4.0% |
| Sulphur | c.0.85% |

*DAF: Dried Ash Free

- Hazard Identification

Classification - Non Hazardous

Potential Health Hazard

This product is inert and low level exposure is not regarded as being hazardous to health.

Occupational Exposure Standard [OES] 8 hour time weighted average for respirable dust 	= 	2mg/m3 [EH 40/98].

May cause irritation to eyes

4.	First Aid Measures

| Eyes | Irrigate thoroughly with water; if discomfort persists seek medical attention. |
| --- | --- |
| Lungs | Remove from exposure. |
| Skin | Wash off thoroughly with soap and water. |
| Mouth | Wash out mouth thoroughly with water. |

5.	Fire Hazard

No fire hazard when stored at ambient temperatures. Non-combustible under normal circumstances. Anthracite has a very high ignition temperature (700-800o c).

Low hazard in the form of dust if exposed to flame or heat, produces carbon monoxide when burnt in a restricted supply of oxygen.

Fire Fighting

Use water or foam to fight fire.

However, do not attempt to use water in enclosed spaces as further flammable gasses may be 	generated.

- Accidental Release/Spillage.

No hazard or contamination of water courses other than slight temporary discolouration,   Disposal Considerations

Sweep up spillage.

7.	Handling and Storage

Handle packaging with care, do not use sharp hooks to lift bags, always lift Bulk Bags using lifting loops in a safe manner with suitable equipment.

Store away from oxidizing agents.

Storage should be away from direct sunlight and kept dry under cover.

The material has an unlimited shelf life and does not deteriorate if stored dry.

If allowed to become wet, the product will not flow readily from storage bag.

8.	Exposure Controls / Personal Protection

Maintain adequate ventilation, especially in confined areas. When handling wear dust particulate respirators – FFP1 EN149:2001, sturdy gloves, safety glasses/goggles, protective workwear and safety footwear.

9.	Physical Characteristics

Appearance	...	...	Black, Shiny, Granular.

Nominal Sizing	...	...	Between 0.5mm - 14mm (according to Grade/Size).

Bulk Density	...	...	650 -750 kg/m3  	               (according to Grade/Size).

Solubility in Water	...	Nil.

10.	Stability and Reactivity

Stable under normal conditions, avoid excessive heat and flames. No reaction with water. Avoid contact with Oxidising Agents.

11.	Toxicological Information

No known toxicological effects from this product.

12. 	Ecological Information

This product has no known eco-toxicological effects

13. 	Disposal Considerations

There are no specific disposal instructions for this product, non hazardous inert mineral.

14.	Transportation

No hazard labeling required.								Shipping description – Granular Anthracite.							Shipping name – Puracite.

15.	Regularity Information

This product conforms to EN12909-2012 for drinking water treatment and may be used without the approval of Government Authorities.

16.	Other information

Ensure all national/local regulations are observed.

The information on this data sheet is based on current knowledge and experience and 	customers should ensure that the product is entirely suitable for their own purposes.

There are no known health Hazards.

Prepared by EGL Puracite Ltd. -For further information, please visit our website at http//www.eglpuracite.com

This Safety Data Sheet has been established in accordance with the applicable European Directives. Details given in this document are believed to be correct at the time of printing. Whilst proper care has been taken in the preparation of this document, no liability for injury or damage resulting from its use can be accepted.